## Slide 1: Philips MRI spiral reconstruction problem
By Emiel Hartsema
K.E.Hartsema@student.tudelft.nl

## Slide 2: Emiel Hartsema
Working on advanced reconstruction algorithm for multicomponent magnetic fingerprinting
Email: K.E.Hartsema@student.tudelft.nl
Master project applied physics TU Delft

## Slide 3: Code on github
A python notebook has been uploaded to my github to show code used.
Link to github: https://github.com/EmielHartsema/philips-reconstruction-problem/blob/main/Philips%20spiral%20MRI%20problem.ipynb

## Slide 4: Reconstruction algorithm
To test, I made a simple reonstruction algorithm, same as shown in sigpy turotial [1]
[1] https://github.com/mikgroup/sigpy-mri-tutorial/blob/master/01-gridding-reconstruction.ipynb
Dicom image supplied with dataset

## Slide 5: Reading kspace data
Data read from datafile with matlab script
Output format is as expected (i.e. correct num of coils, num images, num datapoints per spiral, num spirals per image)
Python version gives exactly same resulting complex matrix
Reading kspace data does not seem to be the problem

## Slide 6: Generating kspace coordinates
Parameters used (as given in settings file)
  FOV: 208 mm
  spirals per image = 48;
  acq. window (ms) = 5.0;
  spiral direction = "spiral out";
  variable density = No
Sampling tau calculated from acq window and #samples (1210).
  5/1210 = 0.00413223
Oversampling ratio = 1
Spiral variable frequency scale – CSC parameter = 3.0

## Slide 7: Generating kspace coordinates
Interleaf generated with spiralblur2018.py (Code on github [1])
Interleafs are rotated 2pi/48 * ky (counter clock wise)
ky from the .list file [0,1,2,…,47]
First interleaf starts in +x direction
[1] https://github.com/EmielHartsema/philips-reconstruction-problem/blob/main/Philips%20spiral%20MRI%20problem.ipynb

## Slide 8: Density compensation
Density compensation based on a paper linked below
Hoge, R. D., Kwan, R. K. S., & Pike, G. B. (1997). Density compensation functions for spiral MRI. Magnetic Resonance in Medicine, 38(1), 117–128. https://doi.org/10.1002/mrm.1910380117

## Slide 9: Reconstrucion of simulated data
Data simulated with spiral coordinates
Works well, density compensation seems to be correct.
Single coil images
Original
Reconstruction

## Slide 10: Reconstrucion of real data
No phantom is visible, even in the single coil images.
Single coil images
Root sum square of coil images

## Slide 11: NUFFT
Because the error is already present in the single coil images, the input to the NUFFT must be incorrect.
K-space data has been calculated in two independent ways, so is probably correct
Oversampling ratio stated to be 1 in file.
Coordinates: unsure

## Slide 13
Insert a picture

## Slide 14
Insert a picture